## Slide 1
Borivoje Nikolić
University of California, Berkeley
bora@eecs.berkeley.edu
Chipyard:
Integrated RISC-V SoC Design, Simulation, Implementation Environment

## Slide 2: Generators Enable Specialization, Lower Design Cost
Digital: Chisel3
CHISEL: Constructing Hardware In Scala Embedded Language
  Open-source hardware construction language
  Software library whose classes represent hardware primitives
  Methods connect the classes together
  So executing the software constructs a graph representing the RTL
Compiles to FIRRTL
Emits Verilog + collaterals
v.3.4 is current
CHISEL/FIRRTL have graduated!
  Moved to CHIPS Alliance
J. Bachrach, et al, DAC 2012
Analog: BAG2 / BAG3
Open-source Python-based framework allowing executable specification of design procedure
Includes family of layout APIs enabling process-portable but designer-controlled analog layout generators
J. Crossley, et al, DAC 2013
E. Chang, et al, CICC 2018

## Slide 3: Berkeley RISC-V ISA
www.riscv.org
An open, license-free ISA
  Runs GCC, LLVM, Linux distributions, glibc, …
  RV32, RV64, and RV128 variants for 32b, 64b, and 128b address spaces
Base ISA only ~40 integer instructions
Extensions provide full general-purpose ISA, including IEEE-754/2008 floating-point
Designed for extension, customization
Developed at UC Berkeley, maintained by RISC-V Foundation
Most of cost of chip development is in software, so want to make sure software is reused across many chip designs
Many research and commercial cores offered
  Pulpino
  Rocket
Rocket is an example of a generator written in Chisel

## Slide 4: Chisel+BAG-Generated RISC-V Chips
Jun
May
Raven-1
Raven-2
Raven-3
Raven-4
EOS14
EOS16
EOS18
EOS20
EOS22
EOS24
2011
2012
2013
2014
2015
May
Apr
Aug
Feb
Jul
Sep
Mar
Nov
Mar
SWERVE
Apr
Hurricane-1
2016
Jul
Mar
Hurricane-2
CRAFT-0
2017
FFT2
CraftP1
Raven, Hurricane: ST 28nm FDSOI, SWERVE: TSMC 28nm EOS: IBM 45nm SOI, CRAFT: 16nm TSMC, Beagle, Hydra: Intel 22FFL
Chisel3+BAG2
EAGLE
2018
AI
2019
ADCS
Mar
EAGLEX
GPS
FADER
BAG
Chisel2
Chisel
Verilog
BEAGLE
2020
HYDRA

## Slide 5: We Have Generated a Lot of Stuff!
Many open source components:
Goal: Make it easy for small teams to design, integrate, simulate, validate workload performance and tape-out a custom SoC
Chisel
FIRRTL
RISC-V
Rocket Core
BOOM Core
TileLink
Accelerators
Caches
Peripherals
Diplomacy
Configuration System
FireSim
HAMMER
BAG

## Slide 6: Chipyard
Chipyard
Tooling
Chisel
FIRRTL
RISC-V
Rocket Chip
Generators
Rocket Core
BOOM Core
TileLink
Accelerators
Caches
Peripherals
Diplomacy
Configuration System
Flows
FireSim
HAMMER
Software RTL Simulation
BAG
BAG Modules

## Slide 7: Foundational Components
Rocket Chip SoC generators
  Parameterization system
  Component composability
  SoC system integration
  TileLink/Diplomacy interconnect
Chisel / FIRRTL
  Productivity through object-oriented/functional meta-programming for HDL
  IR transforms to enable single-source multi-platform.

## Slide 8: What is Rocket Chip?
A highly parameterizable SoC generator
  Replace default Rocket core w/ your own core
  Add your own coprocessor
  Add your own SoC IP to uncore
A library of reusable SoC components
  Memory protocol converters
  Arbiters and Crossbar generators
  Clock-crossings and asynchronous queues
The largest open-source Chisel codebase
  Scala allows advanced generator features
Developed at Berkeley, now maintained by many
  SiFive, CHIPS Alliance, Berkeley
In industry: SiFive Freedom E310

## Slide 9: Structure of a Rocket Chip SoC
Tiles: unit of replication for a core
  CPU (Rocket, BOOM, Ariane/CVA6)
  L1 Caches
  Page-table walker
L2 banks:
  Receive memory requests
FrontBus:
  Connects to DMA devices
ControlBus:
  Connects to core-complex devices
PeripheryBus:
  Connects to other devices
SystemBus:
  Ties everything together

## Slide 10: Generators Integration
Cores
  Rocket, BOOM
  Sodor
  Ariane (CVA6)
Accelerators
  Hwacha
  Gemmini
  Educational: SHA3
  NVDLA
Memory System
  SiFive’s Last-Level Cache
Peripherals
  Icenet
  SiFive Blocks
  Testchip IP

## Slide 11: Customization
Cores and controllers: Intra-core Rocket/BOOM configurations
  Control core / PMU as an example
Simple RoCC accelerators
  SHA3 as a demo
Complex RoCC accelerators
  Hwacha and Gemmini as examples
MMIO Tilelink accelerators
Peripherals

## Slide 12: Simulation/Implementation Targets
Custom hardware design is not just about generated IP blocks!
Different collaterals for different simulation or implementation targets
  Design cycle RTL simulation
  Verification / Validation
  VLSI flow
  FPGA prototyping

## Slide 13: Software
Compatible standard RISC-V Tools versions
ESP-Tools as a non-standard equivalent SW tools package with custom accelerator extensions (Hwacha, Gemmini)
Libgloss based bare-metal tests
FireMarshal workload and Linux distro management
Notes: While basic RISC-V software has stabilized and been upstream (mostly the GNU toolchain, and major components of LLVM),it is still sometime requires to use the newest versions of the tools, and find compatible toolchains (for example, in the content of new standard extension like the vector extensions). Furthermore, specific accelerator require modification to the software toolchains (binutils) or the ISA simulator (spike). Chipyard maintains the old “riscv-tools” model to provide a set of compatible software tools. It uses a parallel esp-tools set for a custom toolchain for the non-standard extensions and accelerators available in chipyard.

## Slide 14: Chipyard 1.4 Updates

## Slide 15: OpenSBI Integration
OpenSBI – Open-source implementation of RISC-V Supervisor Binary Interface (SBI) specifications.
  PMP Support, Missing CSR emulation, Misaligned load/store
  Flexible, layered approach
OpenSBI Integration - OpenSBI as the default bootloader in Chipyard
  Helps to avoid SBI implementation fragmentation
  Broader community support than bbl
  bbl remains as an option for legacy workloads
Western Digital: https://riscv.org/wp-content/uploads/2019/06/13.30-RISCV_OpenSBI_Deep_Dive_v5.pdf
Notes: OpenSBI's appeal over bbl is the additional flexibility:
1. It follows a Linux-like device model that makes writing drivers more modular.
2. Platform-specific code can be added through hooks.
3. It can be used as a static library in other bootloaders/firmware (as can bbl but which is less well-documented).

## Slide 16: HarnessBinders
IOBinders: generalized abstraction for IO interfaces from the chip perspective
  IOCells for test-chip tapeout
  Bridges for FireSim simulations
  Passthrough wires for digital software RTL simulation
HarnessBinders: generalized abstraction for IO interfaces from the test environment perspective
  SystemVerilog harness for software RTL simulation
  FireSim Harness with Golden Gate Passes
  FPGA “shell” for local FPGA prototyping
  FMC / host FPGA softcore interface for FPGA-teathered test-chip bringup
Help converge pre-silicon and post-silicon testing environments

## Slide 17: Local FPGA Prototyping
FPGA prototyping vs. FPGA simulation/emulation
Initial support for VCU118 and Arty-7
Based on SiFive FPGA-shells
  Enables expansion to additional FPGAs supported by fpga-shells
  HarnessBinders
Can be used for test-chip bringup
  Testing using SonicBOOM FPGA host
Future work includes PCIe-based interface and FireSim support
Notes: Highlight Abe’s beagle demo uses this.

## Slide 18: MultiClock Support
Diplomatic clocking
Multiclock config fragments
  Bus frequency specification
  Crossing specification
Divide-only PLL model multiclock simulation harness (FireSim, VCS, Verilator)
  Automatically compute highest common frequency
class MulticlockRocketConfig extends Config(
new freechips.rocketchip.subsystem.WithNBigCores(1) ++
new chipyard.config.WithTileFrequency(1600.0) ++
new chipyard.config.WithSystemBusFrequency(800.0) ++
new chipyard.config.WithMemoryBusFrequency(1000.0) ++
new chipyard.config.WithPeripheryBusFrequency(100) ++
new chipyard.config.WithSystemBusFrequencyAsDefault ++
new chipyard.config.WithCbusToPbusCrossingType(AsynchronousCrossing()) ++
new chipyard.config.WithSbusToMbusCrossingType(AsynchronousCrossing()) ++
new freechips.rocketchip.subsystem.WithRationalRocketTiles ++
new testchipip.WithAsynchronousSerialSlaveCrossing ++
new chipyard.config.AbstractConfig)

## Slide 19: Unified Generator Improvements
Use Chipyard configs in FireSim build recipes
  No need to duplicate configurations within the FireChip environment
Override default UART baudrate in FireChip
  Smoother experience when adjusting peripheral frequency
[firesim-boom-singlecore-nic-l2-llc4mb-ddr3]
DESIGN=FireSim
TARGET_CONFIG=WithNIC_DDR3FRFCFSLLC4MB_WithDefaultFireSimBridges_
WithFireSimConfigTweaks_chipyard.LargeBoomConfig
PLATFORM_CONFIG=F65MHz_BaseF1Config
instancetype=z1d.2xlarge
deploytriplet=None

## Slide 20: Hammer: VLSI Flow
Improved Makefile-based Hammer integration with Chipyard
  “single-click” gate-level simulation for RISC-V binaries
  “single-click” full-chip simulation-based power estimation
OpenRoad nangate45 Hammer backend
  Skywater 130 support in progress
Improved VLSI flow documentation
RISC-V Binary
Chipyard-based SoC Config
Synthesis
Place-and-Route
Gate-level Simulation
Power Estimation
make CONFIG=… BINARY=…

## Slide 21: Generator Upgrades
Chisel 3.4, FIRRTL 1.4
  Improved generated names
  Improved verification APIs
  Annotation handling improvements
Sodor Core Integration
  Used for education and classes
  Core integration documentation
Gemmini 0.5
  GEMM Hardware FSM
  Floating-point scaling
  Transposer, im2col

## Slide 22: Enabling Complete Open Source Agile SoC Design

## Slide 23: Mixed Signal Roadmap
Initial exploration of mixed-signal block integration
  BAG2 vs. BAG3 vs. BlackBox approaches
Majority of existing generators are in BAG2
  Time-interleaved ADC, SerDes, PLLs, …
  TSMC16, TSMC28, Intel22, GF14
BAG3-migration path
  SKY130 (open source)
  Intel22, GF12
PLL and ADC generators to be (re-)open-sourced

## Slide 24: Open Source Community Support
Open-source EDA ecosystem tooling support
  Skywater 130nm flow support for complete open-source
  Generator-to-GSDII
  OpenRoad integration as an open-source VLSI EDA flow
Hammer enables migration between the technologies

## Slide 25: Conclusion

## Slide 26: Community
RISC-V Summit talks using Chipyard
Education
  Used (successfully) in 3 classes during Spring 2020
  Used in 4 classes during Spring 2021
Notes: External (RISC-V Summit talks)
Internal (Education)

## Slide 27: Berkeley EE192/290C Course
https://github.com/ucb-bar/chipyard
Processor core, interfaces
Software tools
https://www.chisel-lang.org/
Custom BLE digital baseband, accelerator wrappers
Berkeley Analog Generator (BAG) - generated SAR ADC
20 students designing a5th year M.S 28nm SOC: Rocket+AES+BLE 3rd-, 4th-yr undergrads,. students, first-year Ph.D.s and two more senior
No prior chip design experience!

## Slide 28: Community
Documentation
  Over 100 pages!
  chipyard.readthedocs.io
  Talks about heterogeneous SoCs, adding Verilog IP, accelerators, etc.
Tutorials
  MICRO 2019 Tutorial
  RISC-V Summit 2019 Tutorial
  (Almost) ASPLOS 2020 tutorial
  ESSCIRC 2020 Tutorial
  ISCA 2021 Tutorial
Mailing list
  ~200 threads

## Slide 29: Summary
Chipyard 1.4 has been released
  Github: https://github.com/ucb-bar/chipyard/
  Docs: https://chipyard.readthedocs.io/en/latest/index.html
  Mailing List: https://groups.google.com/forum/#!forum/chipyard
Integrated design, simulation and implementation framework
Roadmap to converging the various flows

## Slide 30: Summary
We have made it easy to design specialized SoCs
Automated mapping into cloud FPGAs, ASICs
ASIC implementation requires access to proprietary tools and technologies
  Open-source movement may enable easier-to-port ASIC tutorials
  Skywater 130nm is an open-source PDK

## Slide 31: Join The Community!
Used in industry and academia
Development is all open-source and on Github
  Stable `master` branch (latest release)
  Less-stable `dev` branch with all the newest features
Sub-projects managed using submodules
Over 100 pages of documentation!
  If something isn’t clear, please let us know
We appreciate feedback! We appreciate PRs even more!

## Slide 32: Learn More
Chipyard
  Github: https://github.com/ucb-bar/chipyard/
  Docs: https://chipyard.readthedocs.io/en/latest/index.html
  Mailing List: https://groups.google.com/forum/#!forum/chipyard
FireSim
  Website: https://fires.im/
  Github: https://github.com/firesim/firesim/
  Docs: https://docs.fires.im/en/latest/
  Mailing List: https://groups.google.com/forum/#!forum/firesim

## Slide 33: Acknowledgments
Faculty: K. Asanovic, E. Alon, J. Bachrach, V. Stojanovic, D. Patterson
Staff: B. Richards, C. Markley, J. Lawson, J. Dunn
Students (current and past): Brian Zimmer, Yunsup Lee, Ben Keller, Paul Rigge, Angie Wang, Stevo Bailey, Eric Chang, Pi-Feng Chiu, Colin Schmidt, John Wright, Martin Cochet, Albert Ou, Howard Mao, Woorham Bae, Jaeduk Han, Andrew Waterman, Henry Cook, Christopher Celio, Adam Izraelevitz, Zhongkai Wang, Sean Huang, Zhaokai Liu, Sagar Karandikar, Alon Amid, Nathan Narevsky, Jaehwa Kwak, Donggyu Kim, David Biancolin, Jack Koenig, Abraham Gonzalez, Ben Korpan, Jerry Zhao, Daniel Grubb, Harrison Liew,…
Intel Agile ISTC
DARPA CRAFT, PERFECT, RTML programs
STMicroelectronics, TSMC chip donations, fabrication