## Slide 1: Chisel and FIRRTL for next-generation SoC designs
Jack Koenig SiFive CWG TAC Member

## Slide 2: Table of Contents
Introduction
Highlights
Looking Forward

## Slide 3: Introduction
What is the Chisel Working Group (CWG)?

## Slide 4: What is Chisel?
Constructing Hardware In a Scala Embedded Language
Domain Specific Language where the domain is digital design
NOT high-level synthesis (HLS) nor behavioral synthesis
Write Scala program to construct and connect hardware objects
  Parameterized types
  Object-Oriented Programming
  Functional Programming
  Static Typing
Intended for writing reusable hardware generators (libraries)

## Slide 5: No Loss of Expressibility: “Verilog-like” Chisel
FIR Filter - 3-point moving average
What about >3 points? What about weighted averages?
We want a generic FIR filter!

## Slide 6: Massive Increase in Parameterizability: “Software-like” Chisel
FIR Filter - Parameterized by bitwidth and coeffients with no loss of expressibility or performance.
Meta-programming enables powerful parameterization.

## Slide 7: Massive Increase in Parameterizability: “Software-like” Chisel
FIR Filter - Parameterized by bitwidth and coeffients with no loss of expressibility or performance.
Meta-programming enables powerful parameterization.

## Slide 8: Platform-Specific or Application-Specific RTL Changes
IBM 45nm SOI
ST 28nm FDSOI
Zynq FPGA
Chip RTL
+ scan interface
+ snapshotting
+ interactive debug
+ clock-generators
+ SRAMs with init
+ specialized layout
+ SRAM macros
+ modified module hierarchy
+ specialized layout
8

## Slide 9: Realization: We need a software stack, but for hardware
libraries
language
compiler
platforms
projects
x86
ARM
RISC-V
transforms
clang
Hwacha
Rocket
BOOM
rocketchip
chisel-utils
FIRRTL
Chisel Frontend
Notes: Reminder that Aliaksei pointed out that we emit Verilog and there’s “the rest of the owl” beneath that (unlike what LLVM emits), important shout outs to Verilator, Open FPGA and OpenROAD for doing the hard work of making Verilog useful.

## Slide 10: FIRRTL: An Extensible Hardware Compiler Framework
Modular Compiler Passes (Transforms)
Top
MyMux
...
...
Top
MyMux
...
...
Top
MyMux
...
...
Core
Transform
Custom
Transform
Metadata
Annotations
Metadata
Annotations
Metadata
Annotations
Robust Metadata/Annotations Support

## Slide 11: Projects of the Chisel Working Group
Chisel 3
FIRRTL
ChiselTest (formerly Chisel Testers 2)
Treadle
Chisel IOTesters
DSP Tools
Diagrammer
Chisel Bootcamp
Chisel Template
Currently a CHIPS Alliance “Sandbox” project with intent to ”Graduate”

## Slide 12: Highlights
(From the last six months)

## Slide 13: Repos moved to CHIPS Alliance Github

## Slide 14: Further Improved Website
3/29/21
14
Community page
www.chisel-lang.org
Now with a search bar!
Latest API Docs
Project-specific documentation

## Slide 15: Further Improved Website
3/29/21
15
www.chisel-lang.org
Documentation examples are compiled and run!!!

## Slide 16: More Releases
Improved methodology started with 3.2.0
More frequent minor releases
Minor releases maintain binary compatibility
Overlapping major release branches
  3.2.8 released after 3.4.1
[Still] working towards faster release cadence
SNAPSHOT releases are automatically published for every push to stable branches
Many thanks to Chick Markley and Jim Lawson at Berkeley

## Slide 17: Enhanced Signal Naming (from last time)
Historically Chisel has struggled with signal naming
Chisel 3.4 has much better naming
Old* Verilog
Chisel 3.4 Verilog
Notes: user control

## Slide 18: Refined Signal Naming
Optional “tap” output
What should the name of the port be?
  port
  tap_port
  tap
  tapPort
In 3.4.0, the name was ”tap_port”
In 3.4.1 on, the name is “tap”
Additional improvements to naming (especially when using recursion)
Now with ~5 months of use, it’s going great!
Notes: user control, users are deleting their .suggestNames

## Slide 19: Recent Tapeouts / News
Google - Skywater - Efabless shuttle included [at least] 3 Chisel designs:
  Spectrometer - https://github.com/milovanovic/spectrometer
  Crypto Accelerator - https://github.com/asinghani/crypto-accelerator
  Ibtida SoC - https://github.com/hadirkhan10/caravel_ibtida_soc
An Eight-Core 1.44 GHz RISC-V Vector Machine in 16nm FinFet (ISSCC)
  https://ieeexplore.ieee.org/document/9365789
SiFive HiFive Unmatched
  https://www.sifive.com/boards/hifive-unmatched
More? 🤷‍♂️

## Slide 20: Looking Forward

## Slide 21: Improved FPGA support
Historically, Chisel has been used primarily for ASICs
It has been difficult to take advantage of FPGA-only features out-of-the-box
  Memory initialization
  Register initialization
  BRAM inference
Coming --target:fpga option will box up features that improve FPGA support
Chisel v3.4.4
Don’t forget about me!

## Slide 22: AutoCloneType2
cloneType is an implementation detail that leaks into the user API
User-defined types need to implement it
Original AutoCloneType (aka “Reflective AutoCloneType”) works well but has some limitations
  Parameters must be defined as “vals”
  Works in typical use cases but not all use cases
  Slow
The Chisel compiler plugin can now generate cloneType methods, with none of those limitations
Chisel v3.4.3
.cloneType
I’m a TLBundle!

## Slide 23: DataView
Often users want to manipulate hardware values as if they were a different type
  AXI-style flat bus interface used as more structured hierarchy
  Manipulate 1D Array of Reg as if it were 2D
Similar to a ”union” in SystemVerilog or C
  Raw bits mapping may not correspond 1:1
Similar to “façade pattern” in OOP
  Very boilerplate heavy
Similar to a “conversion” in Functional Programming
  Conversions are immutable though, need to manipulate underlying representation
Best analogy is a “View” in SQL
Much more powerful than casts in Chisel today
Work In Progress

## Slide 24: Chisel Community Conference China 2021
WHERE: ShanghaiTech University, Pudong District, Shanghai, China
WHEN: June 25 to June 26, 2021
Co-located with first annual RISC-V Summit China
Keep an eye on https://www.chisel-lang.org/ for more details including call for submissions!

## Slide 25: What Else?
Continued work on verification
  Experimental SMT Backend
  Several projects working on formal verification
    Specification
    Bindings to formal checkers
    Report / counterexample generation
  Constrained random stimulus generation
  Software-based VIPs
Better and more documentation
Scala 2.13 support slated for Chisel 3.5
Vec literals
Better connection semantics
🚀

## Slide 26: Get Involved
www.chisel-lang.org
Chat with us on Gitter
Ask questions on StackOverflow
Watch talks on YouTube

## Slide 27: Extra Slides

## Slide 28: Improved Release Methodology
major
major
Backport
Backport
Backport
major
Backport
3.2.x
master
3.3.x
3.3.0
3.2.1
3.2.0
Automated Backporting + CI
3.2-SNAPSHOT
3.3-SNAPSHOT
3.5-SNAPSHOT