## Slide 1: Chisel and FIRRTL for next-generation SoC designs
Jack Koenig SiFive CWG TAC Member

## Slide 2: Introduction
What is the Chisel Working Group (CWG)?

## Slide 3: What is Chisel?
Constructing Hardware In a Scala Embedded Language
Domain Specific Language where the domain is digital design
NOT high-level synthesis (HLS) nor behavioral synthesis
Write Scala program to construct and connect hardware objects
  Parameterized types
  Object-Oriented Programming
  Functional Programming
  Static Typing w/ Powerful Type Inference
Intended for writing reusable hardware generators (libraries)

## Slide 4: No Loss of Expressibility: “Verilog-like” Chisel
FIR Filter - 3-point moving sum
What about >3 points? What about weighted averages?
We want a generic FIR filter!
Notes: You may notice a few differences from Verilog
No explicit clock or reset?
Common case of single clock/reset domain is easy, more control also available

## Slide 5: Massive Increase in Parameterizability: “Software-like” Chisel
FIR Filter - Parameterized by bitwidth and coeffients with no loss of expressibility or performance.
Meta-programming enables powerful parameterization.

## Slide 6: Massive Increase in Parameterizability: “Software-like” Chisel
FIR Filter - Parameterized by bitwidth and coeffients with no loss of expressibility or performance.
Meta-programming enables powerful parameterization.

## Slide 7: Platform-Specific or Application-Specific RTL Changes
IBM 45nm SOI
ST 28nm FDSOI
Zynq FPGA
Chip RTL
+ scan interface
+ snapshotting
+ interactive debug
+ clock-generators
+ SRAMs with init
+ specialized layout
+ SRAM macros
+ modified module hierarchy
+ specialized layout

## Slide 8: Realization: We need a software stack, but for hardware
libraries
language
compiler
platforms
projects
x86
ARM
RISC-V
transforms
clang
Hwacha
Rocket
BOOM
rocketchip
chisel-utils
FIRRTL
Chisel Frontend
Notes: Reminder that Aliaksei pointed out that we emit Verilog and there’s “the rest of the owl” beneath that (unlike what LLVM emits), important shout outs to Verilator, Open FPGA and OpenROAD for doing the hard work of making Verilog useful.

## Slide 9: FIRRTL: An Extensible Hardware Compiler Framework
Modular Compiler Passes (Transforms)
Top
MyMux
...
...
Top
MyMux
...
...
Top
MyMux
...
...
Core
Transform
Custom
Transform
Metadata
Annotations
Metadata
Annotations
Metadata
Annotations
Robust Metadata/Annotations Support

## Slide 10: Projects of the Chisel Working Group
Chisel 3
FIRRTL
ChiselTest (formerly Chisel Testers 2)
Treadle
Chisel Bootcamp
Chisel Template
Chisel IOTesters
DSP Tools
Diagrammer

## Slide 11: Highlights

## Slide 12: Chisel v3.5.0 – v3.5.2 Released!
Lightning Highlights
  Vec literal support
  Scala 2.13 support (2.11 EOL)
  Decoder + minimizer API in chisel3.util (w/ Espresso integration)
  Source locator compacting
  Many performance improvements
    Chisel ~40-50% faster, FIRRTL ~20% faster
  New Utilities – Gray code, scanLeftOr
  RTL-IL backend
See release notes on Github!

## Slide 13: Chisel v3.5.0 – v3.5.2 Released!
Lightning Highlights
  Vec literal support
  Scala 2.13 support (2.11 EOL)
  Decoder + minimizer API in chisel3.util (w/ Espresso integration)
  Source locator compacting
  Many performance improvements
    Chisel ~40-50% faster, FIRRTL ~20% faster
  New Utilities – Gray code, scanLeftOr
  RTL-IL backend
Digital Design with Chisel 3rd ed. by Martin Schoeberl
  https://www.imm.dtu.dk/~masca/chisel-book.html
  Also in Chinese, Japanese, and Vietnamese!
See release notes on Github!

## Slide 14: ChiselTest Improvements
Simpler peek/poke with Scala types
Improved Verilator simulation performance via JNA
Verilator backend now supports dumping FST instead of VCD
PeekPokeTester compatibility API
  Helps migrate users off old chisel-iotesters
Simulation constructs can now be annotated
assert/assume/cover graduated out of experimental
Simulation binary caching
Support for bounded model checking (next slide)

## Slide 15: Native Formal Verification Support
Formal verification is assumed to be difficult for users
Good tooling and sensible defaults can help
  Similar to simulator-based flow
  Safe past function
  Automatic reset guarding (default but disableable)
Close integration with simulation testing flow
  Same basic APIs
  Same IDE and tooling integration
Automatically runs counter examples through a simulator to provide a waveform
Native FIRRTL -> SMTLib or btor2 output
Works with Z3 and CVC4
See Kevin Laeufer’s WOSET Paper https://woset-workshop.github.io/WOSET2021.html#article-3

## Slide 16: Native Formal Verification Support
Formal verification is assumed to be difficult for users
Good tooling and sensible defaults can help
  Similar to simulator-based flow
  Safe past function
  Automatic reset guarding (default but disableable)
Close integration with simulation testing flow
  Same basic APIs
  Same IDE and tooling integration
Automatically runs counter examples through a simulator to provide a waveform
Native FIRRTL -> SMTLib or btor2 output
Works with Z3 and CVC4
See Kevin Laeufer’s WOSET Paper https://woset-workshop.github.io/WOSET2021.html#article-3
Notes: This example verifies that when a Chisel memory with synchronous read port and WriteFirst behavior has a read and a write access to the same address, the new value will be returned. The check fails if WriteFirst is substituted with ReadFirst or Undefined (Section IV). It is based on a Verilog example from a popular blog. In the Chisel version, the assertion is automatically delayed until at least one cycle after reset, when there are valid past values available (Section VI). A bounded model check is executed by the verify command, which is called from a standard Scala unit test (Section III). When the check fails, the failing inputs and starting states are replayed on a simulator, resulting in a waveform file that is identical to the output we would get from a dynamic verification run. However, since we used bounded model checking to find the failing trace, it will be as short as possible. In our example, two cycles after reset are needed to fail the property. The first cycle contains the read and write requests and the second cycle observes the arbitrary result on the read port if we set the memory behavior to Undefined for read/write conflicts. The included screenshot was obtained with the open-source GTKWave waveform viewer.

## Slide 17: Definition / Instance
Historically, Chisel elaborates every module instance and then deduplicates structurally equivalent modules
New experimental API for definining (and elaborating) a module once and instantiating multiple times
  Definition – Elaborates implementation of module
  Instance – Merely instantiates public API
Major performance optimization for very large or hierarchical designs
Composes with cross-module reference annotations
Experimental – undergoing active development
See https://www.chisel-lang.org/chisel3/docs/cookbooks/hierarchy.html for docs
Notes: Why is this complicated? What is a public API?

## Slide 18: Definition / Instance
Historically, Chisel elaborates every module instance and then deduplicates structurally equivalent modules
New experimental API for definining (and elaborating) a module once and instantiating multiple times
  Definition – Elaborates implementation of module
  Instance – Merely instantiates public API
Major performance optimization for very large or hierarchical designs
Composes with cross-module reference annotations
Experimental – undergoing active development
See https://www.chisel-lang.org/chisel3/docs/cookbooks/hierarchy.html for docs
Notes: Why is this complicated? What is a public API?

## Slide 19: Definition / Instance
Historically, Chisel elaborates every module instance and then deduplicates structurally equivalent modules
New experimental API for definining (and elaborating) a module once and instantiating multiple times
  Definition – Elaborates implementation of module
  Instance – Merely instantiates public API
Major performance optimization for very large or hierarchical designs
Composes with cross-module reference annotations
Experimental – undergoing active development
See https://www.chisel-lang.org/chisel3/docs/cookbooks/hierarchy.html for docs
Notes: Why is this complicated? What is a public API?

## Slide 20: DataView
Often users want to manipulate hardware values as if they were a different type
  AXI-style flat bus interface used as more structured hierarchy
Allows treating objects of one type as another
A superpowered union or cast, like View in SQL
Used to implement:
See https://www.chisel-lang.org/chisel3/docs/explanations/dataview.html for docs

## Slide 21: DataView
Often users want to manipulate hardware values as if they were a different type
  AXI-style flat bus interface used as more structured hierarchy
Allows treating objects of one type as another
A superpowered union or cast, like View in SQL
Used to implement:
  Seamless integration with Scala types
See https://www.chisel-lang.org/chisel3/docs/explanations/dataview.html for docs

## Slide 22: DataView
Often users want to manipulate hardware values as if they were a different type
  AXI-style flat bus interface used as more structured hierarchy
Allows treating objects of one type as another
A superpowered union or cast, like View in SQL
Used to implement:
  Seamless integration with Scala types
  Bundle upcasting
See https://www.chisel-lang.org/chisel3/docs/explanations/dataview.html for docs

## Slide 23: DataView
Often users want to manipulate hardware values as if they were a different type
  AXI-style flat bus interface used as more structured hierarchy
Allows treating objects of one type as another
A superpowered union or cast, like View in SQL
Used to implement:
  Seamless integration with Scala types
  Bundle upcasting
  User-defined mappings between types
See https://www.chisel-lang.org/chisel3/docs/explanations/dataview.html for docs

## Slide 24: DataView
Often users want to manipulate hardware values as if they were a different type
  AXI-style flat bus interface used as more structured hierarchy
Allows treating objects of one type as another
A superpowered union or cast, like View in SQL
Used to implement:
  Seamless integration with Scala types
  Bundle upcasting
  User-defined mappings between types
  Strip io_ prefix
See https://www.chisel-lang.org/chisel3/docs/explanations/dataview.html for docs
New in 3.5.3

## Slide 25: Realization: We need a software stack, but for hardware
libraries
language
compiler
platforms
projects
x86
ARM
RISC-V
transforms
clang
Hwacha
Rocket
BOOM
rocketchip
chisel-utils
FIRRTL
Chisel Frontend
Notes: Reminder that Aliaksei pointed out that we emit Verilog and there’s “the rest of the owl” beneath that (unlike what LLVM emits), important shout outs to Verilator, Open FPGA and OpenROAD for doing the hard work of making Verilog useful.

## Slide 26: It is a lot of work to build and maintain a software stack
libraries
language
compiler
platforms
projects
x86
ARM
RISC-V
transforms
clang
Hwacha
Rocket
BOOM
rocketchip
chisel-utils
FIRRTL
Chisel Frontend
Metadata /
Annotations
Custom
Infrastructure
Notes: Reminder that Aliaksei pointed out that we emit Verilog and there’s “the rest of the owl” beneath that (unlike what LLVM emits), important shout outs to Verilator, Open FPGA and OpenROAD for doing the hard work of making Verilog useful.

## Slide 27: It is a lot of work to build and maintain a software stack
libraries
language
compiler
platforms
projects
x86
ARM
RISC-V
transforms
clang
Hwacha
Rocket
BOOM
rocketchip
chisel-utils
FIRRTL
Chisel Frontend
Metadata /
Annotations
Shared
Infrastructure
Custom
Infrastructure
CIRCT
Multiple
Dialects
Notes: Reminder that Aliaksei pointed out that we emit Verilog and there’s “the rest of the owl” beneath that (unlike what LLVM emits), important shout outs to Verilator, Open FPGA and OpenROAD for doing the hard work of making Verilog useful.

## Slide 28: What is MLIR?
“Multi-Level IR”
A generalization of LLVM
  Part of the LLVM project
Infrastructure for building new compilers
Suitable for building new IRs
Can handle multiple IRs at once
Written in C++
Extremely performant

## Slide 29: CIRCT: Circuit IR for Compilers and Tools
What is CIRCT (pronounced “circuit”)?
An LLVM incubator project
Compiler infrastructure for generating Verilog
A collection of hardware dialects
  FIRRTL Dialect
  SystemVerilog Dialect*
  RTL Dialects
    Combinational
    Sequential
    Hardware
  Timing Insensitive Dialects
    Elastic Silicon Interconnect (ESI)
    Handshake
A collection of tools for compiling circuits
  e.g., firtool is a drop in replacement for firrtl

## Slide 30: What does this mean for Chisel?
Next generation FIRRTL compiler
Faster compilation (5-10x)
Less memory (5-10x)
Better Verilog emission
Robust platform for new features
Starting in Chisel 3.6
  Built-in support for CIRCT
Starting in Chisel 3.7
  Closer integration with CIRCT
  CIRCT-first features
Chart: Large OOO Compile Time (seconds)
| December | Today (w/ CIRCT)
Chisel | 160.68 | 83.89
FIRRTL | 473.3 | 62.19
7.6x
1.9x
4.3x
Notes: Combined 4.3x

## Slide 31: Community

## Slide 32: Get Involved
www.chisel-lang.org
Chat with us on Gitter
Ask questions on StackOverflow
Watch talks on YouTube
Also check out CIRCT
circt.llvm.org

## Slide 33: Extra / Old Slides

## Slide 34: AutoCloneType2
cloneType is an implementation detail that leaks into the user API (since original Chisel)
Useless boilerplate
Original AutoCloneType works okay but has some limitations
  Parameters must be defined as “vals”
  Works in typical use cases but not all use cases
  Slow
The Chisel compiler plugin now generates cloneType for all Bundles
Available in Chisel v3.4.3 (opt-in)
  Improved in v3.4.4
  Mandatory in v3.5.0
Before:
After:
Notes: I told you about this last time but there’s just _more_

## Slide 35: Further Improved Website
4/19/22
35
Community page
www.chisel-lang.org
Now with a search bar!
Latest API Docs
Project-specific documentation

## Slide 36: Further Improved Website
4/19/22
36
www.chisel-lang.org
Documentation examples are compiled and run!!!

## Slide 37: Enhanced Signal Naming (from last time)
Historically Chisel has struggled with signal naming
Chisel 3.4 has much better naming
Old* Verilog
Chisel 3.4 Verilog
Notes: user control

## Slide 38: Refined Signal Naming
Optional “tap” output
What should the name of the port be?
  port
  tap_port
  tap
  tapPort
In 3.4.0, the name was ”tap_port”
In 3.4.1 on, the name is “tap”
Additional improvements to naming (especially when using recursion)
Now with ~5 months of use, it’s going great!
Notes: user control, users are deleting their .suggestNames

## Slide 39: Improved Release Methodology
major
major
Backport
Backport
Backport
major
Backport
3.2.x
master
3.3.x
3.3.0
3.2.1
3.2.0
Automated Backporting + CI
3.2-SNAPSHOT
3.3-SNAPSHOT
3.5-SNAPSHOT